VATEL             ACC-3000             G.SHDSL

Modulation

- TC PAM

Transmission Medium

- One pair of copper wire

Data Rate

- Manual selectable Rate from 192K, 256K, 384K, 512K, 768K, 1024K, 1168K, 1280K, 1544k, 2048K, 2312K

| ACC3000 |
| --- |
| Physical Description |  |  |
| 35mm(H)×210mm(W)×193mm(D) 914g |  |  |
| System Interaction |  | Network Interface |
| Using a terminal or PC to the CID port Using the LCD of front panel |  | Ethernet Remote Bridge (10/100 Base T Port) RS-449/RS-530 T1/E1 (G.703) V.35 |
| System Configuration |  |  |
| STU-C: Shelf type or Standalone type. STU-R: Standalone type. |  |  |

| Specification |  |  |
| --- | --- | --- |
| Self type |  |  |
|  | Number of cards: | 16 slots, one MIU plus up to 15 G.SHDSL line cards |
|  | Port density: | 1 port/line card |
|  | Network interface: | Ethernet, EIA-530, T1 and E1; V.35, RS-449 and X.21 needs conversion cable |
|  | Connection: | Front access for Management and Network interface |
|  | Management: | LED indicators |
|  |  | CID/RS232 |
|  |  | SNMP agent, management IP control list |
|  |  | Telnet/Web-based GUI |
|  | NMS: | Snmp-based GUI manager |
|  | Power requirement: | -36VDC~-72VDC |
|  | Dimension: | 308mm(H)×483mm(W)×336mm(D) |
|  | Loop connection: | RJ-45 or Wire wrap pins |
| Standalone type |  |  |
|  | Number of G.SHDSL lines | One line per unit |
|  | Network interface: | Ethernet, EIA-530, T1 and E1; V.35, RS-449 and X.21 needs conversion cable |
|  | Management: | LED indicator, Power, DSL, Link, Alarm, Test and other CID/RS-232 |
|  | Power requirement: | 100V~240 VAC |
|  | Dimension: | 35mm(H)×210mm(W)×193mm(D) |
|  | Loop connection: | RJ-45 |
| Loop Interface |  |  |
|  | Number of wire | Two wires |
|  | Standard | Comply ITU-T G.991.2 Annex A and B |
|  | Line impedance | 135 ohms |
|  | Payload rate | 192K, 256K, 384K, 512K, 768K, 1024K, 1168K, 1280K, 1544k, 2048K, 2312Kb/s for V.35 and Ethernet interfaces |
|  | Transmission distance | 4.1~7.1 km (0.4 mm wire) |
| Ethernet Interface |  |  |
|  | Bridge support | 4k hash table |
|  | Payload rate | N×64kb/s, 3≦N≦36 |
|  | Connector | RJ-45 |
| V.35 Interface |  |  |
|  | Data rate | N×64kb/s, 3≦N≦36 |
|  | Clock source | Internal, DSL or DTE |
|  | Connector/Role | ISO-2593 female/DCE |
| E1 Interface |  |  |
|  | Line code/interface | HDB3/ITU-T G.703.2 MB/s |
|  | Frame format | Framed and transparent |
|  | Payload rate | N×64kb/s, 3≦N≦32 |
|  | Line impedance & connector | DB 15 pin for 120 ohms |
| T1 Interface |  |  |
|  | Line code/interface | B8ZS, AMI/ANSI T1.403, 1.544 Mbps |
|  | Frame format | SF, ESF and Transparent |
|  | Payload rate | N×64kb/s, or N×56kb/s 3≦N≦24 |
|  | Line impedance & connector | DB 15 pin for 100 ohms |
| Environment |  |  |
|  | Storage Temperature | -40℃~60℃ |
|  | Storage Humidity | 5%~95% |
|  | Operating Temperature | 0℃~60℃ |
|  | Operating Humidity | 5%~95%, none condense |
| Maintenance |  |  |
|  | V.54 remote loopback | Built-in |
|  | QRSS pattern generator | Built-in |